## Slide 1
Multi-Site Sizing Overview
2 clusters sized independently
Cluster | Model | Nodes | Cores | RAM | Usable Storage
Site A | HE151 | 8 | 88 | 4048 GB | 119.04 TB
Site B | HE500 | 4 | 252 | 4072 GB | 57.6 TB

## Slide 2
Cluster: Site A

## Slide 3
Current Environment
—
Hosts
0
Total Cores
96
Total Threads
0
Total GHz
400.0
Total RAM
1.0 TB
Peak CPU %
0%
Avg CPU %
0%
Peak Memory %
0%
Avg Memory %
0%
Avg IOPS
0
Peak IOPS
0
NIC Speed
10 GbE

## Slide 4
Workload Analysis
40 active VMs of 44 total
Total vCPUs
180
Provisioned RAM
900 GB
Used RAM
0 GB
Provisioned Storage
0 TiB
Datastore Used
22.5 TiB
Datastore Total
0 TiB

## Slide 5
Proposed: HE151
8 nodes — 1 cluster — 1U — single
Per Node | 
CPU | 1 x Xeon 4310
Cores | 12
Threads | 24
RAM | 512 GB
Storage | 4x 7.68TB NVME
Net IOPS | 150,000
Cluster Total | 
Cores | 88
Threads | 192
GHz | 230.4
RAM | 4.0 TB
RAW Storage | 245.76 TB
Usable Storage | 119.04 TB
Net IOPS | 1,200,000
N-1 Available | 
Cores | 77
Threads | 168
GHz | 201.6
RAM | 3.5 TB
Usable Storage | 119.04 TB
Net IOPS | 1,050,000
vCPU : Core Ratio at N-1
3.77 : 1
Net IOPS = raw 300,000/node − 35% derating = 195,000 ÷ 1.3× RF write-amp = 150,000/node, × 8 nodes.

## Slide 6
Sizing Rationale
HE151
How this was sized
Determined by CPU performance — this cluster delivers 104% of your current environment's compute demand (rated throughput scaled to 30% measured peak utilization, grown to the horizon); the node count was raised to clear that floor.
Each bar is 100% of the full cluster: solid = today's load, light hatch = growth + snapshot reserve the workload is sized to, dark hatch = HA failover capacity held back so the cluster still meets the workload with one node down (N-1).

## Slide 7
Capacity Planning — 5 Year Projection
10% YoY growth — 20% snapshot overhead — Growth factor: 1.611x — CPU sizing: N-1
Resource | Current | Year 5 Projected | Proposed (N-1) | Headroom
vCPUs | 180 | 290 | 77 cores @ 3.8:1 | +0 vCPU capacity
RAM | 900 GB | 1.4 TB | 3.5 TB | +2.0 TB
GHz | 120.0 | 193.3 | 201.6 | +8.3 GHz
Storage | 22.5 TB | 47.91 TB (incl. snapshots) | 119.04 TB usable | +71.13 TB
Growth Rate
10% per year
Growth Factor
1.611x over 5 years
Snapshot Overhead
20% base → 32.2% at year 5
This configuration meets all projected requirements through year 5.
Note: 5-year projections are estimates based on assumed linear growth rates and should not be taken as guarantees. Actual capacity needs will depend on business changes, application evolution, market trends, and workload characteristics.

## Slide 8
Cluster: Site B

## Slide 9
Current Environment
—
Hosts
0
Total Cores
96
Total Threads
0
Total GHz
400.0
Total RAM
1.0 TB
Peak CPU %
0%
Avg CPU %
0%
Peak Memory %
0%
Avg Memory %
0%
Avg IOPS
0
Peak IOPS
0
NIC Speed
10 GbE

## Slide 10
Workload Analysis
40 active VMs of 44 total
Total vCPUs
180
Provisioned RAM
900 GB
Used RAM
0 GB
Provisioned Storage
0 TiB
Datastore Used
22.5 TiB
Datastore Total
0 TiB

## Slide 11
Proposed: HE500
4 nodes — 1 cluster — 1U — single
Per Node | 
CPU | 2 x Xeon 6338
Cores | 64
Threads | 128
RAM | 1.0 TB
Storage | 4x 7.68TB NVME
Net IOPS | 150,000
Cluster Total | 
Cores | 252
Threads | 512
GHz | 614.4
RAM | 4.0 TB
RAW Storage | 122.88 TB
Usable Storage | 57.6 TB
Net IOPS | 600,000
N-1 Available | 
Cores | 189
Threads | 384
GHz | 460.8
RAM | 3.0 TB
Usable Storage | 57.6 TB
Net IOPS | 450,000
vCPU : Core Ratio at N-1
1.53 : 1
Net IOPS = raw 300,000/node − 35% derating = 195,000 ÷ 1.3× RF write-amp = 150,000/node, × 4 nodes.

## Slide 12
Sizing Rationale
HE500
How this was sized
Determined by Storage — 47.9 TB required, vs 57.6 TB available at N-1 (20.2% headroom).
CPU performance floor: this cluster delivers 238% of your current environment's compute demand (clock 238%), sized to its 30% measured peak CPU utilization.
Each bar is 100% of the full cluster: solid = today's load, light hatch = growth + snapshot reserve the workload is sized to, dark hatch = HA failover capacity held back so the cluster still meets the workload with one node down (N-1).

## Slide 13
Capacity Planning — 5 Year Projection
10% YoY growth — 20% snapshot overhead — Growth factor: 1.611x — CPU sizing: N-1
Resource | Current | Year 5 Projected | Proposed (N-1) | Headroom
vCPUs | 180 | 290 | 189 cores @ 1.5:1 | +0 vCPU capacity
RAM | 900 GB | 1.4 TB | 3.0 TB | +1.6 TB
GHz | 120.0 | 193.3 | 460.8 | +267.5 GHz
Storage | 22.5 TB | 47.91 TB (incl. snapshots) | 57.6 TB usable | +9.69 TB
Growth Rate
10% per year
Growth Factor
1.611x over 5 years
Snapshot Overhead
20% base → 32.2% at year 5
Based on current projections, some resources may need to be expanded before year 5.
Note: 5-year projections are estimates based on assumed linear growth rates and should not be taken as guarantees. Actual capacity needs will depend on business changes, application evolution, market trends, and workload characteristics.